Note: The installation shown below is for the SPAREBUMPER but the installation process works with all models.

| SPAREBUMPER | INSTALLATION INSTRUCTIONS If you have any problems call us at 1-952-882-8800. |
| --- | --- |
| Parts List: Qty: 1 Hitch Step 2 Rubber Compression Springs 2-3 Rubber Spacers 4 – 1 1/2” Rubber Compression Springs Optional Items (may or may not be included): Locking Hitch Pin Decal | 318 or 424 Model Hitch Step 2 Rubber Compression Springs (Outside) 4- 1 1/2” Rubber Springs (Inside) Rubber Spacers |
| Installation: Step 1. Measure the distance from the center of the 5/8” pin hole to the outside edge of your receiver hitch-photo( The distance will be anywhere from 1½” to 2½ inches. On 80% of the vehicles, this distance will be 2½”. If the distance is 2½” read the installation tips below first then go to Step 2. If the distance is less then 2 ½” read installation tips below and go to Step 3. Step 2. A. Remove packaging. B. Grease the slotted tube end – top, bottom & sides. C. Insert the bumper into the receiver, push the bumper towards vehicle to line up holes & pin it (5/8” pin). See installation tips below. Step 3. A. If the distance from the pin hole to the outside is less than 2 1/2” slide on rubber spacers as needed to keep the compression distance approx. 3/8”. B. Grease the slotted tube end – top, bottom & sides. C. Insert the bumper into the receiver hitch and push towards vehicle & pin it. See installation tips below. |  |
| Installation Tips 1. The SPAREBUMPER is made so that the external rubber springs will have tension on them. You will have to push the bumper approx. 3/8” towards the vehicle while inserting the hitch pin. The first installation will take some effort to push hard enough to line up the holes. (Make sure inner rubber springs don’t slide ahead and block the pin hole.) 2. When the pin hole distance is less than 2½”, add the rubber spacers to keep the compression distance approx. 3/8”. Spacers can be added between the rubber springs or on either end. Note: If you want to remove the bumper, you will have to push it towards the vehicle. Compressing eliminates A, B, C, and D below. 3. Grease the slotted tube end (from slot to end). Although the grease helps as a lubricant for movement, it is mainly used to prevent rust. Once a year, remove the bumper and re-grease. On new vehicles, you may not need to grease the first year. |  |
| The patented compression system eliminates: A. rattles, B. the need for a $20 anti-rattle device, C. keeps the bumper level and D. is a deterrent to theft (locking pin recommended). Note: All springs will “set” over time and lose some of their length. Once they have been in for a while it will be easier to remove and re-install. Save the extra spacers in case you want to add some extra compression. The more it can be compressed the less it will rattle and the more level it will stay. | One Final Note: If you are having some trouble pushing hard enough and you have one of those ratchet style cargo straps, take one hook and attached it to the hook on the receiver hitch (where you’d attach the chains if towing), wrap the strap around the front and hook the other end of the strap on the other receiver hitch hook. Ratchet up until the holes line up. Just make sure you put a towel or something to protect the front of the bumper to eliminate any scratches. Ratchet Strap Installation help on the back side. Happy Trails – Be Safe |
|  | Place one hook on the receiver hitch (where you’d attach the chains if towing), wrap the strap around the front and hook the other end of the strap on the other receiver hitch hook. |
|  | Place a towel or something to protect the front of the bumper to eliminate any scratches. |
|  | Ratchet Up Until Holes Line Up. |
|  | Pin Holes Are Now Lined Up. Put your locking pin in receiver hitch and lock it in place. Then release the strap. |
|  | Final Installation Note: All springs will “set” over time and lose some of their length. Once they have been in for a while it will be easier to remove and re-install. Save the extra spacers in case you want to add some extra compression. The more it can be compressed the less it will rattle; the more level it will stay and the less chance there will be of someone stealing it if you’re not using a locking pin. The patented compression system eliminates: A. rattles, B. the need for a $20 anti-rattle device, C. keeps the bumper level and D. is a deterrent to theft (locking pin recommended). |

# Text boxes

Push To Insert

Grease Entire Area Side-Top-Bottom